STM 32 DRIVER DEVELOPMENT BY FASTBIT

20-aprl-23
# SECTION 01 INTRO

20-aprl-23
# SECTION 02 DEV BOARD USED

20-aprl-23
# SECTION 03 HARDWARE & SOFTWARE REQ.

20-aprl-23
# SECTION 04 IDE INSTALLATION

21-aprl-23
# SECTION 05 CREATING A PROJECT USING STM32UCBEIDE
## 14. SWV working principle :-
- Using printf output on ARM cortex M3/M4/M7 based MCU.
  - This discussion is only for ARM cortex M3/M4/M7 based MCU.
  - Printf works over SWO pin (Serial Wire Output) of SWD interface.

The ITM (INSTRUMENTATION
TRACE MACROCELL UNIT)
is an optional application driven trace source that supports printf style debugging to trace operating system adn application events and generates diagnostic system information

ARM cortex M4 processor

ITM

DEBUG CONNECTOR

SWD 2 pin (debug) +1 pin (trace).

Printf();
Printf imp. In std. Lib
printf()
{
__write();
}

Your project
__write()
{
ITM_SendChar();
LCD_SendChar();
}

29-aprl-23
# SECTION 15 TESTING HELLO WORLD THROUGH SWV

- Copy “code example & paste to sysCalls.c file”.
- Comment “_io_putchar()” & call “ITM_SendChar(*ptr++);”
  Note:- not working with Linux”
  test with discovery kit, debugger might be faulty.

30-aprl-23
# SECTION 16 OPEN OCD AND SEMIHOSTING TO USE PRINTF

- SET LINKER ARGUMENTS
  Some Points
  - exclude syscall.c file
  - error:- “target is not halted”
  - soln:- reset controller just after pressing the debug button
  - -Specs = rdimon_specs -k -Irdimon
- add semi-hosting run command
  - monitor arm semihosting enable
- add the below function call to main.c
  - extern void intialize_monitor_handle(void);
  - initalize_monitor_handles(void);

07-may-23
# SECTION 17 DEBUG OPTIONS

## EMBEDDED CODE DEBUGGING OPTIONS
- Serial wire viewer and data tracking (printf style)
- Single stepping, stoppping over & stepping out.
- Break points.
- Disassembly.
- Call stack
- Expression and Variable window.
- Memory browser.
- Data watch points.

## SWV AND ITM BASED PRINT STYLE DEBUGGING
- ITM trace sourse of ARM cortex M3/M4 processor supports printf style debuggin to trace os and application sevents and emits diagonostic information for your application which can be captured on host IDE to analyse application behaviour even when the application is running.
- Introduced very minimal time-space overhead.

07-may-23
# SECTION 18 SINGLE STEPPING
- Perspective
- Step into, step out/return, step over.
- Instruction stopping mode (for assembly language stepping).

07-may-23
# SECTION 19 DISASSEMBLY & REGISTER WINDOW
- Registers
  - for disassembly

07-may-23
# SECTION 20 BREAKPOINTS
NOTE:-	I know everything about breakpoints.

07-may-23
# SECTION 21 EXPRESSIONS AND VARIABLES
- Hover courser over variable.
- Variable window.
- Expression window (you can also write some expression like “variable + 1” in expression window).

07-may-23
# SECTION 22 MEMORY BROWSER WINDOW
NOTE:-	I KNOW IT.

07-may-23
# SECTION 23 CALL STACK
- Read stack bottom to top.
- Fault analyzer.
  - Read and google. Hard fault -> against the rule of processor
Note:- “signal handler called” in debug window “call stack” always chack fault analyzer.

07-may-23
# SECTION 24 DEBUG WATCH POINTS
- Data watch points (stop whenever vairable trying to change, it depends upon settings).
  - Inside BP window.

07-may-23
# SECTION 25 SFR WINDOW
- SFR (special function register) (memory map register)
  - you can control sfr via SFR window only, without writing any code.
    Exp.-	Modifying GPIO or Enabling clock etc.

07-may-23
# SECTION 26 OTHER FEATURES OF IDE

07-may-23
# SECTION 27 UNDERSTANDING MEMORY MAP
- Memory map of the MCU (stm23f507x)
  - ARM cortex M4
    - width of 32 bit system bus
    - the processor can provide 232 of diffrent addresses (4gb).
  - Each & every priphiral has its own start & end boundry address which can be found on refference manual of MCU.

07-may-23
# SECTION 28 UNDERSTANDING MEMORY MAP
Memory map of the MCU (tiva MCU).
Q:-	how to find base address of register?
A:-	base_____end,

<- End address
Base address ->
Hint:-	base address is always smaller than end-address.

# RANDOM QUERYS
## # TYPE OF MEMORY IN MCU.
- RAM ->	SRAM, DRAM, SDRAM (volatile).
- ROM ->	MASKED ROM, PROM, EPROM (non volatile).
- HYBRID ->	EEPROM, NAND FLASH, NOR FLASH, NV RAM, FRAM, PCM/PCAM (hybrid)
### #1 SRAM
SRAM and DRAM are volatile memory, sram provides extremly fast access time to the processor about frou times than DRAM. The memory also retains its data as long as it has electrical power. Use less power but more expensive than DRAM, SRAM is often use in embedded on as system on a chip or MCU chip, use transistors.

#2	DRAM